## Slide 1
PARcast: E_s(PAR) breadboard wiring
Surface reference sensor: top-down view on a prototyping breadboard
5
10
15
20
25
30
35
40
45
50
55
60
+
–
+
–
a
a
b
b
c
c
d
d
e
e
f
f
g
g
h
h
i
i
j
j
5
10
15
20
25
30
35
40
45
50
55
60
ADS1115
16-bit ADC
VDD
GND
SCL
SDA
ADDR
ALRT
A0
A1
A2
A3
DS3231
Real-time clock
Vin
GND
SCL
SDA
SQW
32K
RST
Teensy 4.1
GND
3V3
19 (SCL0)
18 (SDA0)
Apogee SQ-500
PAR sensor (0–40 mV, self-powered)
Serial 1559+: White / Black / Clear (grey)
White → A0
Black → A1
Clear (grey) → GND (shield)
Wire legend
Red — 3.3 V
Black — GND
Yellow — SCL (I2C clock)
Blue — SDA (I2C data)
White — SQ-500 signal +
Gray dashed — SQ-500 shield
Notes
• I2C bus shared by ADS1115 and DS3231
• ADS1115 address 0x48, DS3231 address 0x68
• Teensy SDA0 = pin 18, SCL0 = pin 19
• SQ-500 differential: reads A0 − A1
• SQ-500 is self-powered, no Vcc
• microSD lives in Teensy built-in slot
PARcast — github.com/LoriAzniveBerberian/PARcast
Built-in microSD slot
USB
on right end

## Slide 2
E_s(PAR) connection table
Authoritative pin-by-pin reference for build and debug
From | Pin / wire | To | Pin / wire | Wire color | Purpose
Teensy 4.1 | 3V3 | Breadboard | Top + rail | Red | Main 3.3 V distribution
Teensy 4.1 | GND | Breadboard | Top – rail | Black | Main ground distribution
Top + rail | — | ADS1115 | VDD | Red | ADC power
Top – rail | — | ADS1115 | GND | Black | ADC ground
Top + rail | — | DS3231 | Vin | Red | RTC power
Top – rail | — | DS3231 | GND | Black | RTC ground
Teensy 4.1 | Pin 18 (SDA0) | ADS1115 | SDA | Blue | I2C data
Teensy 4.1 | Pin 18 (SDA0) | DS3231 | SDA | Blue | I2C data (shared bus)
Teensy 4.1 | Pin 19 (SCL0) | ADS1115 | SCL | Yellow | I2C clock
Teensy 4.1 | Pin 19 (SCL0) | DS3231 | SCL | Yellow | I2C clock (shared bus)
SQ-500 | White wire | ADS1115 | A0 | White | Sensor signal positive
SQ-500 | Black wire | ADS1115 | A1 | Black | Sensor signal negative
SQ-500 | Clear shield | Bottom – rail | — | Gray (dashed) | Shield to ground
Notes on bench testing
• Run I2C scanner sketch: both 0x48 (ADS1115) and 0x68 (DS3231) must appear.
• If only one address shows, check SDA/SCL jumpers and common ground.
• SQ-500 is self-powered: never connect it to a voltage rail.
• Teensy pins 18/19 (SDA0/SCL0) are on the right-side header; count from the USB end.